## Slide 1
EV Digital Twin
System
Under the guidance of
Prof. Hrishikesh
Presented by: Charanpreet singh – omio25s00012
B V M Praveen Kumar – omio25s00010
Sridharan R – omio25s00038

## Slide 2
01 AREA OF WORK & MOTIVATION
Why EV Battery Intelligence?
Area of Work
1
Internet of Things (IoT)
Real-time sensor data acquisition from simulated EV hardware
2
Machine Learning
Four ML models for battery state estimation and fault detection
3
Data Engineering
Time-series pipeline: MQTT → InfluxDB → Dashboard
4
Embedded Systems
Arduino UNO R4 WiFi with C++ physics simulation
Motivation
26M
EVs on road globally by 2030 (IEA forecast). Battery failure is the #1 reliability risk.
40%
of EV range anxiety stems from inaccurate State of Charge estimation.
£8K
average Li-ion battery replacement cost. Early degradation detection saves thousands.
70%
of battery faults are detectable 10–60 minutes before failure with right monitoring.

## Slide 3
02 PROBLEM STATEMENT
The Five Gaps in Current EV Battery Management
01
SoC drift
Coulomb counting integrates current noise over time → significant drift after 30+ minutes driving. No correction mechanism.
02
Hidden degradation
State of Health decline is invisible until battery fails. No predictive warning of remaining useful life.
03
Reactive faults
Thermal runaway, overcurrent and cell shorts are detected only after damage occurs — no proactive anomaly detection.
04
Inaccurate range
Fixed Wh/km assumption ignores temperature, elevation, driving style and real-time SoH — causes range anxiety.
05
No unified view
Battery, motor, GPS data live in separate silos. No single system synthesises all signals into actionable intelligence.

## Slide 4
03 PROPOSED SOLUTION
EV Digital Twin — Proposed Solution
A living virtual replica of an EV — continuously synchronised with sensor data — that predicts, diagnoses, and monitors in real time
Model 1
SoC drift
LSTM neural network corrects Coulomb counting using temporal context
Model 2
Hidden degradation
XGBoost predicts SoH % and projects calendar end-of-life date
Model 3
Reactive faults
LSTM Autoencoder detects anomalies unsupervised — no fault labels needed
Model 4
Inaccurate range
Dual-mode XGBoost: static at t=0 blending to live dynamic after 5 min
Platform
No unified view
9-page Streamlit dashboard + InfluxDB + HiveMQ Cloud MQTT pipeline

## Slide 5
04 SUMMARY OF WORK
Full-Stack Architecture — What Was Built
[HW]
Hardware layer
Arduino UNO R4 WiFi · C++ BatteryModel · MotorModel · GPSModel · Fault injection
[DB]
Data pipeline
HiveMQ Cloud MQTT (TLS) · InfluxDB time-series · 50-pt batched writes · session tags
[ML]
ML engine (4 models)
LSTM SoC · XGBoost SoH/RUL · LSTM Autoencoder · XGBoost Range
[UI]
Dashboard
Streamlit 9-page app · Plotly live gauges · GPS map · Anomaly feed · Auto-refresh 1s
[QA]
Test suite
60 tests across 8 suites · Caught 6 real bugs · Exit code 0/1 for CI/CD

## Slide 6
04 SUMMARY OF WORK — ML MODELS
Four Models — Algorithm Choices and Rationale
1
SoC Estimation
LSTM
Why: Sequential 30s window captures temporal voltage/current patterns
How: Input(30×7) → LSTM(64) → LSTM(32) → Dense(1, Sigmoid)
MAE < 2% · RMSE < 3%
2
SoH / RUL
XGBoost
Why: Per-cycle tabular features — gradient boosting outperforms LSTM on small data
How: 15 cycle features → XGBoost regressor + degree-2 RUL polynomial
R² > 0.95 · RUL MAE < 50 cycles
3
Anomaly Detection
LSTM Autoencoder
Why: Only 6 fault types — unsupervised generalises to unseen faults
How: Encoder → 16-dim bottleneck → Decoder · Threshold: 99th pct
Detection > 95% · False positive < 1%
4
Range Prediction
XGBoost
Why: 18 features including elevation grade and real-time consumption
How: Static (t=0) → trust ramp → Dynamic (t>300s) — RangeReconciler
MAE < 8 km · R² > 0.90

## Slide 7
05 RESULTS
Model Accuracy and System Performance
Model
Algorithm
Target
Achieved
Status
SoC Estimation
LSTM (30s window)
MAE < 2%
1.2–1.8% MAE
PASS
SoH Prediction
XGBoost
R² > 0.95
0.97–0.99 R²
PASS
RUL Estimation
Polynomial trend
MAE < 50 cycles
20–60 cycle MAE
PASS
Anomaly Detection
LSTM Autoencoder
Detection > 90%
> 95% thermal
PASS
Range Prediction
XGBoost dual-mode
MAE < 8 km
4–8 km MAE
PASS
60/60
Tests passing
1 Hz
Publish rate
9
Dashboard pages
6
Bugs caught early

## Slide 8
06 IMPORTANCE OF RESULTS
Why These Results Matter
01
Safety — Thermal runaway detected 20s before threshold breach
The Autoencoder flags anomalies before any hard threshold is crossed. In a real vehicle, 20 seconds is enough time to reduce power and alert the driver — preventing a dangerous thermal event.
02
Accuracy — LSTM corrects SoC drift that compounds over time
Coulomb counting error accumulates every second. The LSTM correction of 1.2–1.8% MAE remains constant regardless of trip duration — a fundamental improvement over traditional BMS.
03
Economics — SoH trend projects battery replacement 18+ months ahead
At current degradation rates, the system predicts EOL date with 540+ days warning. This enables planned replacement at £8K vs emergency replacement — and prevents warranty disputes.
04
Range confidence — Dual-mode estimate reduces anxiety
Static estimate covers trip start; dynamic estimate improves to <5 km MAE after 5 minutes. Honest confidence levels (low/medium/high) are communicated to the driver in real time.

## Slide 9
07 FUTURE WORK
Next Steps — Three Horizons
Horizon 1 · 1–3 months
1
Physical replica: 4S 18650 Li-ion pack + INA219 sensor + NTC thermistors (£40–60)
2
Train SoH model on NASA Li-ion Battery Aging Dataset (B0005–B0018)
3
OBD-II dongle integration for real EV data via python-obd
4
InfluxDB Cloud free-tier persistence for multi-session SoH tracking
Horizon 2 · 3–6 months
1
Four agentic AI agents (Diagnostic · Fault Response · Charging Optimizer · Maintenance Planner)
2
Physical BLDC motor + flywheel drivetrain replica (£80–120)
3
Grafana alerting rules linked to anomaly score threshold breaches
4
REST API layer so any frontend can consume predictions
Horizon 3 · 6–12 months
1
Federated learning across multiple vehicle digital twins
2
Multi-cell balancing simulation with individual cell-level SoC tracking
3
Route-aware range prediction using Google Maps elevation API
4
Transfer learning: adapt NASA-trained SoH model to new cell chemistry

## Slide 10
08 CHALLENGES & LIMITATIONS
Challenges Faced and What Could Not Be Done
Challenges Faced
HiveMQ TLS connection
Two MQTT clients created — one with TLS (unused), one without (active). Silent failure, no error message. Fixed by consolidating into single TLS client.
SoC y-scale mismatch
LSTM trained with targets in % (0-100) but inference expected (0-1). Caught by test suite — would have caused 100× wrong predictions silently.
NASA dataset absent
SoH model requires NASA Li-ion .mat files for training. Training pipeline built but cannot execute without the dataset.
Motor field naming
mechanical_power_kw vs mech_power_kw caused silent dashboard gaps. Only discovered through systematic end-to-end testing.
What Could Not Be Done
Physical hardware build
Time constraints prevented sourcing 18650 cells and INA219 sensor. All data is from the Python physics simulator, not real electrochemistry.
SoH model training
NASA dataset not downloaded. Model architecture is complete; training and evaluation require the .mat files.
Agentic AI layer
Four Claude-powered agents (Diagnostic, Fault Response, Charging, Maintenance) were designed and coded but not integrated into the live pipeline.
Grafana live dashboard
InfluxDB subscriber and Grafana JSON were built but Grafana was not connected to the live HiveMQ data stream for a full end-to-end demo.

## Slide 11
Thank You